## Slide 1: Combimac permanent magnet motor

## Slide 2: Rating data, input
Supply voltage: 650V, 3ph
Rated frequency: 166.7 Hz
Continous Power (2 windings): 131 kW
Power factor: 0.97..0.98
Nominal current (2 windings): 123 A
Maximum current: 123 A (No overload)
Connection: Star
Back EMF: 766V +/- 10%
Inductance L-L 1 winding: 5.88 mH Xdd
Resistance L-L 1 winding: 210 m ohm

## Slide 3: Output
Rated speed: 2000 RPM
Rated torque: 625

## Slide 4: Power and torque curves
Where:
, is motor power [W]
, is motor torque [Nm]
, is motor speed [rad/s]
, is 625Nm up to field weakening
in field weakening
Where:
, is rated torque
, is rated speed
Chart: Power
| 0 | 200 | 400 | 600 | 800 | 1000 | 1200 | 1400 | 1600 | 1800 | 2000 | 2200 | 2400 | 2600 | 2800 | 3000 | 3200 | 3400
 | 0 | 13089.9694 | 26179.9388 | 39269.9082 | 52359.8776 | 65449.8469 | 78539.8163 | 91629.7857 | 104719.7551 | 117809.7245 | 130899.6939 | 130899.6939 | 130899.6939 | 130899.6939 | 130899.6939 | 130899.6939 | 130899.6939 | 130899.6939
Chart: 
| 0 | 200 | 400 | 600 | 800 | 1000 | 1200 | 1400 | 1600 | 1800 | 2000 | 2200 | 2400 | 2600 | 2800 | 3000 | 3200 | 3400
Torque [Nm] | 625 | 625 | 625 | 625 | 625 | 625 | 625 | 625 | 625 | 625 | 625 | 568.1818 | 520.8333 | 480.7692 | 446.4286 | 416.6667 | 390.625 | 367.6471

## Slide 5: Efficiency-η 1/2
4 points given in data sheet
100% load – η=95%
75% load – η=94%
50% load – η=92%
25% load – η=86%

## Slide 6: Efficiency-η 2/2
Used curve fitting, to describe as a function
Where:
a=0.9249
b=0.00028
c=-0.2844
d=-0.05531
x, is load given in percent
See excel document, efficiency PMAC
Chart: 
| 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 95 | 100
f(x) | 0.6394 | 0.70967 | 0.76328 | 0.80426 | 0.83565 | 0.85977 | 0.87838 | 0.89281 | 0.90407 | 0.91293 | 0.91997 | 0.92562 | 0.93023 | 0.93405 | 0.93726 | 0.94002 | 0.94243 | 0.94458 | 0.94654 | 0.94834 | 0.95003

## Slide 7: Construction
Frame size: 200L B5
Mass: 225 kg (estimated)
Bearing: 6313-2Z-C3 (SKF) D.E and N.D.E
Air gap (magnetic): 3 mm
Air gap (mechanical): 2 mm
Ingress protection: IP 56 (5 is dust protection, 6 is powerful waterjets)
Encoder: ECN 113 13 bit (Heidenhain)
Balancing level ISO1940-1, G1
Balancing method ISO21940-32, no key
Rotation viewed on DE: clockwise
Winding 1-2 electric phase shift 30 degrees, winding 2 lagging when looking on shaft

## Slide 8: Stator
Outer diameter: 320 mm
Inner diameter: 230 mm
Core length: 160 mm
No. Coils: 60

## Slide 9: Rotor
Outer diameter: 224 mm
Inner diameter: 150 mm
No. of magnet poles: 10
Magnet material: FeNdB40UH
Inertia: t.b.d kgm2

## Slide 10: Cooling and losses
Method: IC7A1W7
Coolant pressure: 4 bar
Pressure drop: max 0.5 bar
Losses to coolant: 5.7 kW
Losses to air: 0.25 kW
Coolant flow min: 8 l/min
Coolant flow max: 10 l/min
Coolant temp in: 27-34 degrees